## Slide 1
RecycleRight
AI-Powered Waste Sorting System on Jetson Orin Nano
陳發達 (611451001) · 楊瑋竣 (411201107)
Supervisor: Prof. 宋建龍 | Tatung University | I4210 AI Edge Computing Practicum | June 2026

## Slide 2
Problem Statement & Motivation
The Problem
Recycling contamination from wrong-bin deposits is the #1 cause of recyclables going to landfill. Taiwan's source-separation rules require 4 distinct categories. Static signs alone don't work.
Who Benefits
University campuses, cafeterias, office floors — any high-traffic shared space with multi-bin stations. Venue operators, recycling processors, and end-users all benefit.
Why Edge AI on Jetson Orin Nano?
🔒
Privacy
Video never leaves device — no cloud transmission
⚡
Latency
< 30 ms vs 300+ ms cloud round-trip → servo responds instantly
🔌
GPIO/UART
Servo motors need direct hardware control via ESP32
💡
Power
15–25 W always-on vs 150–350 W desktop GPU

## Slide 3
Final System Architecture
SENSE
IMX219 CSI
1280×720 @60fps
GStreamer
nvarguscamerasrc
→
PROCESS
YOLOv8n
TRT FP16
conf ≥ 0.50
~23 ms/frame
→
DECIDE
10-frame vote
≥6 hits wins
lid_ready sync
DONE handshake
→
ACT
ESP32+PCA9685
4× SG90 servo
4× status LED
ffplay audio
4 Concurrent Threads
T1 CameraCapture
T2 Detector
T3 SerialController
T4 HUD/tegrastats
ESP32 (USB UART 115200) → PCA9685 I²C (addr 0x40) → 4× SG90 servo | Sequence: LED ON → 120° → 5s hold → 0° → LED OFF → DONE:<label> | lid_ready Event released

## Slide 4
What Changed vs the Proposal
Model
❌ YOLOv12n (proposed)
✅ YOLOv8n TRT FP16 (shipped)
YOLOv8n has more mature TRT FP16 export on JetPack 6 / TRT 10.7. Same accuracy class, better toolchain stability.
Actuator Control
❌ Direct Jetson GPIO servo
✅ ESP32 + PCA9685 via UART
Decouples servo PWM from Jetson. DONE handshake provides clean mutual exclusion without asyncio complexity.
Messaging
❌ MQTT broker (Mosquitto)
✅ threading.Queue + Event
Single-device deployment — direct Python primitives are lower latency and simpler to test than an MQTT round-trip.
Red rejection LED
❌ GPIO-driven red LED
✅ Removed
GPIO contention with PCA9685 I²C. Low-vote rejections handled by no-action + audio announcement instead.

## Slide 5
AI Model & Optimization Choices
YOLOv8n
Architecture
TRT FP16
Precision
640×640
Input Size
4 classes
Categories
0.50
Conf. Threshold
96.02%
mAP@50
Training & Export Pipeline
Dataset: Custom 12,571 images (10,056 train / 1,257 val / 1,258 test), collected with IMX219 at Tatung University lab. Labeled with Roboflow. Training: PC server, YOLOv8n pretrained COCO, 100 epochs AdamW, best checkpoint at epoch 0 (pretrained weights already excellent). Export: model.export(format='engine', half=True) on-device — TRT engine built for Orin Nano SM 8.7 / TRT 10.7 / CUDA 12.6.

## Slide 6
Implementation
Highlights

## Slide 7
Implementation Highlights
01
MOG2 Motion-Gated Inference
Every frame passes MOG2 background subtraction first (~1 ms CPU). YOLO inference (~23 ms GPU) only runs if a foreground contour exceeds MIN_AREA = 500 px². This gate suppresses > 95% of inference calls on idle frames — the reason live GPU utilization is ~55% rather than saturated, preserving thermal headroom for bursty item presentation.
02
10-Frame Majority Voting + lid_ready Interlock
We accumulate VOTE_FRAMES=10 frames and require VOTE_THRESHOLD=6 (≥60%) agreement before dispatching. Once a command is sent, lid_ready.clear() prevents any further dispatch until the ESP32 sends DONE:<label>\n back. Two layers of false-positive protection: statistical confidence + hardware interlock.
03
TRT FP16 On-Device Export
best.pt (FP32) → best_fp16.engine via model.export(format='engine', half=True) running on the Jetson itself. TRT engines are compiled for a specific SM version and CUDA version — never copy .engine files between machines. Export takes ~3–5 min; loads in <2 s at inference time.

## Slide 8
Implementation Highlights (continued)
04
ESP32 Firmware — Busy Guard & Serial Flush
The busy flag in the Arduino loop() ignores all incoming serial bytes during an active sort cycle. After the servo sequence completes, while(Serial.available()) Serial.read() flushes the buffer before sending DONE: — preventing any queued ghost commands from triggering a second sort. Discovered through direct physical observation: the servo opened twice on a single item.
05
5-Stage CI/CD Pipeline on Self-Hosted Jetson Runner
lint → test (≥90% coverage) → security-scan (bandit + pip-audit) → build (arm64 Docker → GHCR) → integration-test (pulls image on Jetson runner, end-to-end test). The conftest.py mock layer lets all unit tests run on Ubuntu cloud runners with no GPU, camera, or serial port. Only integration-test requires the real Jetson.
UART Protocol:
Jetson → ESP32: PET\n | GLS\n | MTL\n | PAP\n ESP32 → Jetson: DONE:PET bottle\n | DONE:Glass bottle\n | ...

## Slide 9
CI/CD Pipeline — 5-Stage GitHub Actions
lint
ruff check
zero violations
→
test
pytest
≥90% coverage
→
security
bandit
pip-audit
→
build
arm64 Docker
push GHCR
→
integration
Jetson runner
end-to-end
GitHub-Hosted (Ubuntu — no GPU needed)
Self-Hosted Jetson
Trigger
Push to main
+ Pull Request
Coverage
--cov-fail-under=90
93 tests pass
Security
0 high-severity
bandit findings
Image tag
sha-<commit>
+ :latest float
Deploy
Tag v* triggers
deploy.yml
Tag-triggered deploy.yml: git tag v1.0.0 → push → Jetson runner pulls GHCR image → deploy.sh → healthcheck.sh → rollback.sh available (< 30 s to previous tag)

## Slide 10
Test Set & Methodology
Class
Train
Val
Test
Total
PET bottle
5,093
654
673
6,420
Aluminum can
2,557
304
297
3,158
Glass bottle
2,300
255
305
2,860
Tetra Pak
1,820
271
221
2,312
Total instances
11,770
1,484
1,496
14,750
Accuracy Measurement
• model.val() on held-out test split (1,258 images)
• Eval on best.pt FP32 (training server)
• Deploy as best_fp16.engine (< 0.5 mAP drop expected)
• conf=0.50, IoU=0.70
Performance Instrumentation
• FPS: pipeline-level counter in Detector thread
• Latency: time.perf_counter() around model() call
• GPU%/Power: sudo tegrastats --interval 1000
• Parsed by scripts/parse_tegrastats.py → utilization.csv
• 449 samples @ 1 Hz, ≥60 s sustained live run

## Slide 11
Performance Requirements & Optimization Journey
≥25 FPS
Target FPS
≤60 ms
p95 Latency
≥0.80
mAP@50
≤15 W
VDD_IN
≥40% GPU
GPU Utilization
≤60% CPU
CPU Headroom
Step
Change
FPS
p50 ms
GPU%
Power W
Note
Step 0 — FP32
best.pt 15W
39.5
24.8
73%
8.7 W
Baseline
Step 1 — FP16
TRT FP16 15W
43.1
22.9
67%
7.5 W ↓14%
Best power efficiency
Step 2 — 25W
FP16 + 25W mode
44.8
21.2
62%
7.5 W
Marginal +4% FPS
Step 3 — MAXN
FP16 + MAXN mode
44.4
21.8
66%
7.8 W
No gain vs 25W
Step 4 — Live
MOG2 + 4 threads
gated
N/A
55%
10.8 W
Final deployment
★ All 6 targets met: FPS 43.1≥25 ✅ p95 30.2ms≤60ms ✅ mAP 96.02%≥80% ✅ Power 7.5W≤15W ✅ GPU 55%≥40% ✅ CPU 48.5%≤60% ✅

## Slide 12
Results — Accuracy & Performance
96.02%
mAP@50
96.95%
Precision
96.38%
Recall
96.66%
F1 Score
Per-class AP@50
Aluminum can (best)
97.30%
PET bottle
96.19%
Tetra Pak
95.65%
Glass bottle (lowest)
94.95%
Mode
FPS
p50ms
p95ms
15W (FP16)
43.1
22.9
30.2
25W (FP16)
44.8
21.2
31.8
MAXN (FP16)
44.4
21.8
30.9
Live Pipeline (tegrastats, 449 samples)
CPU avg: 32.1% GPU avg: 45.3%
VDD_IN avg: 6,712 mW (6.7 W)
VDD_IN peak: 8,124 mW (8.1 W)
No thermal throttling observed

## Slide 13
LIVE DEMO
Sense → Process → Decide → Act
1. Jetson powered on — tegrastats visible in corner
2. Live IMX219 CSI camera feed — NOT a pre-recorded video
3. YOLOv8n TRT FP16 inference — bounding boxes + FPS counter
4. 10-frame voting window reaches threshold → decision fires
5. SG90 servo opens to 120° — bin lid physically moves
6. Mandarin audio announcement plays — confirms item category
7. ESP32 sends DONE: → lid closes → system unlocks for next item
(Recorded backup available if live setup fails)

## Slide 14
Lessons Learned
1
TRT Engine Must Be Built on Target Device
Tried exporting on laptop (x86 CUDA 11.8) and copying .engine to Jetson → GPU architecture mismatch error. TRT compiles for a specific SM version. Always run export_fp16.py on the Jetson itself. Cost us one full day.
2
GStreamer Pipelines Are Not Portable
nvarguscamerasrc only works on JetPack Jetson systems. Our conftest.py mock layer solved this: mock cv2.VideoCapture at import time → 90%+ coverage on cloud runners with no camera.
3
MOG2 Thresholds Require In-Situ Calibration
MIN_AREA=200 triggered false positives from fluorescent flicker. Raised to 500. The right value depends on camera height, lighting, and bin opening size — cannot be determined from a dataset alone.
4
lid_ready Interlock Was Not in the Original Design
Discovered in integration testing: removing an item before the vote window closed could queue two commands. The Event-based interlock completely eliminates this race condition. Patterns we didn't anticipate during the proposal phase.
5
tegrastats Format Changed in JetPack 6.x
VDD_CPU_GPU_CV replaced POM_5V_GPU. CPU frequency format changed. Our parse_tegrastats.py uses regex fallbacks for both JetPack 5 and 6. Always test parsers against actual log output before trusting numbers.

## Slide 15
What We'd Do Differently
1
Both
Decide INT8 vs FP16 at Week 1, not Week 13. We scaffolded a calibration/ directory but never populated it. Benchmark both on a small test set early and commit to one path.
2
楊瑋竣
Write integration tests before wiring the actuator. We spent Week 13 retrofitting tests around code that was already running on hardware. Contracts first, implementation second.
3
陳發達
Run class-distribution analysis at Week 9, not Week 14. Glass bottle AP was lowest (94.95%). Knowing this earlier would have let us collect more samples while time permitted.
4
陳發達
Pin nvpmodel mode in deploy.sh. During demos we forgot which power mode was active. One line of sudo nvpmodel -m 1 in deploy.sh ensures reproducible performance on every deploy.
5
Both
Register the self-hosted Jetson runner at Week 10, not Week 14. Setup takes 30 minutes. Starting earlier means catching integration failures weeks sooner, when there's still time to fix them.

## Slide 16
Thank You
Questions & Answers
陳發達 (611451001) — Hardware integration, ESP32 firmware, dataset, model training, benchmarking
楊瑋竣 (411201107) — Software architecture, CI/CD pipeline, test suite, parse_tegrastats.py
Anticipate:
❓ Why YOLOv8n over YOLOv12n?
❓ What if the camera disconnects?
❓ How would this scale to 50 devices?
❓ What's the worst failure mode observed?
❓ Walk through what CI does on a PR
GitHub: github.com/phatdattran2k2/recycleright | Supervisor: Prof. 宋建龍 | June 2026